## Slide 1: Gas-Shutoff Sensor Project Proposal
Sponsor: Wesam Khalil advisor: dr. melinda holtzman
Noah Harvey - Alec Wiese - Kam RobertsoN - Arsalan Sabet

## Slide 2: Agenda
Problem Statement
Project Objective
Methodology for Implementation
  Design Phase
  Implementation Phase
  Testing Phase
  Evaluation Phase
Project Schedule Plan
Current Project Progress

## Slide 3: Problem Statement
Methane, more formally known as Natural Gas, can leak from home appliances and hidden gas lines which presents dangerous and potentially deadly environments to the inhabitants of the home.

## Slide 4: Project Objective
The objective of the project is to create a device that turns off the flow of Natural Gas to the home when a leak from a home appliance or gas line is detected in the air.

## Slide 5: Methodology for Implementation
Design Phase
  Gas Sensor provides methane density limit detection (MQ-2)
  Microcontroller to receive gas sensor signal & commands shut-off actuator (PIC12F675)
  Wireless simplex transmission (433MHz)
  Wireless transmission encoder and decoder (PT2262/72)
  Detector in standard single gang in-wall junction box with cover plate

## Slide 6: Methodology for Implementation
Implementation Phase
  Prototype design and assembly
  Detector schematic creation and bill-of-materials (BOM) generation
  Detector and Actuator Printed Circuit Board (PCB) layout and manufacturer order
  Board assembly
  Refine PCB and adjust BOM (if needed)

## Slide 7: Methodology for Implementation
Testing Phase
Prototype
  Detector characteristics and limits
  Microcontroller programming
  Wireless transmission integrity
  Power supply stability
  Actuator functionality
PCB
  Detector and Actuator board and component fitment
  Wireless transmission
  Gas detection and actuator performance
  Board fitment in junction box

## Slide 8: Methodology for Implementation
Evaluation Phase
  Out-of-limit state validation
  System functionality as a complete unit
  Actuator response
  System ease of reproduction
  Critical System Refinement

## Slide 9: Project Schedule Plan
  Researching established market options One Week
  Designing prototype Two Weeks
  Purchasing prototype materials One Week
  Analyzing component datasheets One Week
  Writing functional code Two Weeks
  Testing & debugging prototype Two Weeks
  Creating schematic and PCB layout One Week
  Purchasing PCB components One Week
  Assembling PCB’s One Week
  Testing code with PCB Two Weeks
  Written Report and Presentation Preparation Two Weeks

## Slide 10: Current Project Progress
  Prototype
    Gas Detection (Butane) Successful
    Wireless Transmission – Questionable Signal Integrity
    Microcontroller
      Written in Assembly Language – Move to C Language
      Utilization expansion to wireless encoding
    Actuator is simulated using relay device
      Battery power is not enough to actuate a small solenoid

## Slide 11: Current Project Progress

## Slide 12: Current Project Progress